## Slide 1
Prof. dr. ir. Jan H. Kwakkel
Multi-Actor Systems department
Faculty of Technology, Policy and Management
Model-based support for Decision Making under Deep Uncertainty

## Slide 2: Problem 1
Imagine you are a flood risk manager. You need to decide on an investment in dikes for the coming ten years. You have been given the following information
Chance of a severe flood is 1 in 6
Damage in case of a flood is 1 million
Costs of investment in dikes is 1.3 million
If dikes are built, chance of flood falls below 1 in 50
Assume a 10-year planning horizon
Will you invest in the dikes?

## Slide 3: Problem 2
Imagine you are a flood risk manager. You need to decide on an investment in dikes for the coming ten years. You have been given the following information
According to a first group of experts, the chance of a severe flood is 1 in 6
According to a second group of experts, the chance of a severe flood is 1 in 10
Damage in case of a flood is 1 million
Costs of investment in dikes is 1.3 million
If dikes are built, chance of flood falls below 1 in 50
Will you invest in the dikes?

## Slide 4: So what is deep uncertainty?
Deep uncertainty refers to the situation where the various parties to a decision do not know or cannot agree on
  The system model that relates actions to consequences
  The prior probability distributions to put on the inputs to the system model(s)
  Which consequences to consider and their relative importance
Deep uncertainty often involves decisions made over time in dynamic interaction with the system.
Kenneth Arrow first used the term in the late 1990s to characterize the climate change debate
Formal work on dealing with deep uncertainty started in the early 2000s at the RAND Corporation and TU Delft.
Deep uncertainty is also known as radical uncertainty, Knightian uncertainty, or uncertainty proper

## Slide 5
Notes: Pas op met woord methode
Ontbreken van theorie en effectieve methode

## Slide 6
Notes: Pas op met woord methode
Ontbreken van theorie en effectieve methode

## Slide 7
Notes: Pas op met woord methode
Ontbreken van theorie en effectieve methode

## Slide 8
Notes: Pas op met woord methode
Ontbreken van theorie en effectieve methode

## Slide 9
Notes: Pas op met woord methode
Ontbreken van theorie en effectieve methode

## Slide 10
Notes: Pas op met woord methode
Ontbreken van theorie en effectieve methode

## Slide 11: Why use models?
Argument from complexity
supplement human reasoning
sensitivity to initial conditions
Argument from uncertainty
When confronted with uncertainty, instead of making an assumption, explore the consequences of alternative assumptions systematically to identify differences that make a difference
Notes: Multiplicity of legitimate perspectives
Does l’esprit de geometrie have a place?

## Slide 12: Decision-making under deep uncertainty
  Decision aiding – the aim of decision advise is to facilitate learning about a problem and potential courses of action, not to dictate the right solution. This entails a shift from a priori to a posteriori decision analysis.
  Adaptive planning – plans should be designed from the outset to be adapted over time in response to how the future is unfolding
  Exploratory scenario thinking– the future is uncertain and cannot be probabilistically constrained, we need systematic what-if analysis of the future which serves as a test bed for candidate strategies

## Slide 13: Aiding decision making

## Slide 14: What is the role of models in decision making?
Notes: The task of an adaptive organism is to find the difference between an existing state and a desired state and then find the correlating process that will erase the difference.

## Slide 16: Computer assisted reasoning
Arguments from ensembles
Hypothesis generation
Existence proofs
Non-existence proofs
Reasoning from special cases
Assessing properties of the entire ensemble
Identifying differences that make a difference
  Ranking uncertainties
  Partitioning uncertainty space

## Slide 17: Adaptive planning

## Slide 18: Adaptation pathways
Current
situation
Action
A
Action
B
Action
C
Action
D
Transfer station to new
policy
action
Adaptation Tipping Point of a
policy action
(
Terminal
)
Policy action
effective
Changing conditions
Time high
-
end scenario
Time low
-
end scenario
0
0
10
70
80
90
100
Years
10
70
80
90
100
1
2
3
4
5
9
Pathway
Co
-
benefits
Costs
Benefits
+++
++
0
-
-
-
0
0
0
-
0
+++
+++++
+++
+
+
0
0
0
0
Time horizon
100
years
6
7
8
-
-
-
-
-
+
+++
++++
0
0
+

## Slide 19: Exploratory scenario thinking

## Slide 20
Often, more information can be captured in an ensemble of alternative plausible models than can be captured by any individual model.
Bankes (2002) 10.1073􏰅pnas.092081399

## Slide 21: XLRM framework

## Slide 22: Running a model as a function
X : uncertainties
  Model structure uncertainties as well as exogenous forces
  A point in uncertainty space is called a scenario
L : levers
  A point in lever space is called a policy
  Policies to be tested over the uncertainties
M : outcomes
  Outcomes of interest

## Slide 23: Exploratory modelling in a nutshell

## Slide 24: Exploratory modelling in a nutshell

## Slide 25: Exploratory modelling in a nutshell

## Slide 26: Exploratory modelling in a nutshell: scenario discovery

## Slide 27: Exploratory modelling in a nutshell: scenario discovery

## Slide 28: Exploratory modelling in a nutshell: scenario discovery

## Slide 29: Exploratory modelling in a nutshell: scenario discovery

## Slide 30: Manual scenario discovery exercise

## Slide 31
Click and download as zip file

## Slide 32
Unzip the downloaded file
Open manual_scenario_discovery.html

## Slide 33: Scenario Discovery

## Slide 34: Subspace partitioning
Problem: find an (orthogonal) subspace in the model input space, which has a high concentration of cases of interest
Rule induction problem
Regression vs. (binary) classification
Rule induction algorithms
Classification and Regression Trees (CART)
Patient Rule Induction Algorithm (PRIM
Various other more specialized possibilities

## Slide 35: PRIM

## Slide 36: PRIM
Lenient hill-climbing optimization algorithm
Each step in the optimization is stored  peeling trajectory
Coverage: fraction of cases of interest within the box
Density: fraction of cases in the box which is of interest
Interpretability: number of restricted uncertainties
Quasi p-values: one sided binomial test, proxy for statistical significance of each restricted uncertainty in isolation
Resampling statistic: do random subsets of the same dataset produce essentially the same box?

## Slide 39: Scenario Discovery

## Slide 40: Scenario discovery for designing adaptation pathways
Scenario discovery results can be understood as an n-dimensional generalization of adaptation tipping points
An adaptation tipping point is the level of an exogenous driver at which adaptation is required. These can be mapped to time for different scenarios
Scenario discovery finds n-dimensional boxes in the uncertainty space where a given policy fails
Some caveats
  Not all exogenous drivers change over time
  Mapping scenario discovery results onto the time axis is an open research question

## Slide 41: Scenario Discovery excercise

## Slide 42: Working with Google Colab
Go to Google Colab
upload scenario discovery.ipynb
Upload
  100 experiments.tar.gz
  10000 experiments.tar.gz
Go through the notebook (shift + enter)

## Slide 43: EMA workbench: a python library for RDM
Code: https://github.com/quaquel/EMAworkbench
Documentation: https://emaworkbench.readthedocs.io/en/latest/
pip installable
  pip install ema_workbench[recommended]

## Slide 44
Upload scenario discovery.ipynb

## Slide 45
Open file viewer

## Slide 46
Click upload files

## Slide 47: Working with Google Colab
Go to Google Colab
upload scenario discovery.ipynb
Upload
  100 experiments.tar.gz
  10000 experiments.tar.gz
Go through the notebook (shift + enter)

## Slide 48: Introduction to RDM

## Slide 49: Robust Decision Making
Robust decision making is the process of using computer simulations to iteratively stress test candidate strategies
Decision Framing: structure the decision problem using the XLRM framework
Evaluate strategy across futures: explore behavior of modeled system across the uncertainties for all outcomes of interest, for one or more candidate strategies
Vulnerability analysis: scenario discovery
Tradeoff analysis: if vulnerabilities are limited analyse robustness tradeoffs amongst objectives
New futures and strategies: based on interpretation of 3 and 4, refine XLRM setup

## Slide 50: Experimental designs
Notes: Figures show three sampling strategies with same number of samples (100)
For latin hypercube and monte carlo the red dots show the difference
Problem with full factorial is combinatory explosion.
Problem with lhs is generating it for many cases is memory intensive

## Slide 51: How does a Latin Hypercube work?

## Slide 52: How does a Latin Hypercube work?

## Slide 53: How does a Latin Hypercube work?

## Slide 54: How does a Latin Hypercube work?

## Slide 55: Choosing a distribution
Notes: Slide shows a pragmatic argument for using a uniform distribution, namely exploring the behaviors a model can exhibit, no attempt is made to try and predict

## Slide 56: RDM exercise

## Slide 57: Shallow lake problem
How much anthropogenic pollution to release into the lake, while avoiding that the lake tips into an irreversible eutrophic state?
Adaptive version: what is a state based control rule that tells how much can be released?
Hadka et al (2015). 10.1016/j.envsoft.2015.07.014.

## Slide 58: XLRM structuring of shallow lake problem
Levers parameters characterizing the control rule
Uncertainties
b: decay rate
q: recycling exponent
mean: mean of natural
inflows
stdev: stdev of natural
inflows
delta: discount rate
Outcomes
Maximum pollution level
Utility
Inertia
reliability
Relations

## Slide 59: Working with Google Colab
Go to Google Colab
upload RDM.ipynb
Upload
  lake_model_dps.py
  4policies.tar.gz
  (optional) lake_1000.tar.gz
Go through the notebook (shift + enter)

## Slide 60: Workflow
Connect model to the workbench
  X: uncertainties
  L: levers which parameterize the control rule
  R: model of the shallow lake
  M: outcomes of interest
Develop basic system understanding by exploring the behavior of the system for one or more basic policies (i.e. control rules)
Optimize policies for a reference scenario
Re-evaluate (selected) policies over a much larger ensemble of scenarios
Analyze robustness and vulnerabilities (i.e., scenario discovery)
Iterate if necessary

## Slide 61: Robustness metrics

## Slide 62
McPhail, C., et al (2018). "Robustness metrics: How are they calculated, when should they be used and why
do they give different results?" Earth's Future. 10.1002/2017EF000649

## Slide 63: Robustness metrics
Figure adapted from Trindade et al. (2019) https://doi.org/10.1016/j.advwatres.2019.103442
How to summarize the distribution over scenarios in (preferably) one number?
Robustness per kpi, or one robustness number per policy?
policy
deeply uncertain factor 1
deeply uncertain factor 2
deeply uncertain factor 3
KPI’s per
scenario
Distribution per kpi over scenarios

## Slide 64: 3 families of robustness metrics
Satisficing robustness
Absolute: the observed performance of a policy in each scenario compared to an absolute performance threshold
Regret
Relative: the difference between the observed performance of a policy in each scenario and the performance of some reference policy for each scenario
Descriptive statistics
Characterizing the distribution of performance of a policy over the set of scenarios using one or more moments of the distribution

## Slide 65: Robustness calculation
McPhail, C., et al (2018). "Robustness metrics: How are they calculated, when should they be used and why
do they give different results?" Earth's Future. 10.1002/2017EF000649

## Slide 67: MORDM exercise continued

## Slide 68: Example: Competitive position of the Port of Rotterdam

## Slide 69: The world container model
Tavasszy, L. A., Minderhoud, M., Perrin, J.-F., & Notteboom, T. (2011). A strategic network choice model for global container flows: specification, estimation
and application. Journal of Transport Geography, 19, 1163–1172

## Slide 70: Major uncertainties that might impact the port of Rotterdam

## Slide 71: Identification of vulnerabilities under what conditions does Rotterdam lose throughput?

## Slide 72: Identification of vulnerabilities under what conditions does Rotterdam lose throughput?
Increase of costs on all hinterland connections for ports in the Hamburg – le Havre range
More than 1 additional day required for shipping from Rotterdam
No substantial decrease in hinterland transport costs for Rotterdam
Together, these 3 factors explain 75% of the cases where Rotterdam loses throughput, with 71% accuracy

## Slide 73: Worst case discovery
Is there a perfect storm scenario?
  No, small changes in the uncertain factors do not lead to large change in throughput or transshipment

## Slide 74: Worst case discovery
Is there a perfect storm scenario?
  No, small changes in the uncertain factors do not lead to large change in throughput or transshipment
Under what conditions do the Mediterranean ports become competitive?
    Substantial increase in EU hinterland costs, substantial reduction in port handling costs and hinterland transport costs and time for Mediterranean ports, and the opening of the Northern passage
Limitation: shipping line network structure is kept static

## Slide 75
Income inequality in the Vietnam Mekong Delta
Bramka Arga Jafino
Maaike van Aalst
Notes: Many talk about climate migration from the mekong
But real story is quite more complicated
So we created a simulation model to better understand what is happening and to identify possible interventions that address inequality

## Slide 76
Performance indicators
District level profitability
Integrated assessment model
Uncertainties
river discharge
upstream dam development
farming preferences
drought impacts
Adaptation policies
more high dikes
less high dikes
fertilizer subsidies
seed upgrade
Notes: Walk through the modeling work

## Slide 77: How can income patterns change?
43K scenarios
7 archetypical
income patterns
Classification tree mapping uncertainties and policies to types of income patterns

## Slide 78: How can income patterns change?
43K scenarios
7 archetypical
income patterns
Classification tree mapping uncertainties and policies to types of income patterns

## Slide 79: How sensitive are rankings to normative assumptions?

## Slide 80: Closing remarks

## Slide 81
Kwakkel & Haasnoot (2018) Supporting decision making under deep uncertainty: a synthesis of approaches and techniques